## Slide 1: Fall Protection Awareness Training
Preventing Falls, Protecting Lives

## Slide 2: Why Fall Protection Matters
Falls are a leading cause of workplace fatalities
OSHA consistently ranks fall hazards among top violations
Fall protection saves lives — and prevents serious injuries
This training helps you recognize risks and take action

## Slide 3: Common Fall Hazards
Working at height (roofs, ladders, scaffolds)
Unprotected edges and open holes
Improper use of ladders or lifts
Slippery or unstable surfaces
Lack of guardrails or fall arrest systems

## Slide 4: OSHA Requirements
Fall protection required at:
4 feet in general industry
6 feet in construction
Any height when working over dangerous equipment

## Slide 5: OSHA Requirements
Employers must:
Provide fall protection systems
Train employees on safe use
Inspect equipment regularly

## Slide 6: Types of Fall Protection
Guardrails — passive protection at edges
Safety nets — catch falling workers
Personal Fall Arrest Systems (PFAS)
  Harness
  Lanyard
  Anchor point
Positioning systems — hold worker in place
Warning lines — alert workers to hazards

## Slide 7: Personal Fall Arrest System (PFAS)
Key Components:
  Full-body harness — distributes force
  Lanyard or SRL — connects to anchor
  Anchor point — must support 5,000 lbs per worker
Shock absorber — reduces impact force
Always inspect before use. Never reuse after a fall.

## Slide 8: Ladder Safety Basics
Use ladders on stable, level surfaces
Maintain 3-point contact
Don’t overreach — keep belt buckle between rails
Inspect ladders before each use
Never use the top step unless designed for standing

## Slide 9: Scaffolding Safety
Must be erected by trained personnel
Guardrails required at edges
Platforms must be fully planked
Access ladders or stairs must be provided
Inspect daily before use

## Slide 10: Fall Protection Best Practices
Plan ahead — assess fall risks before starting work
Use the right equipment for the task
Inspect gear before each use
Stay tied off when required
Report damaged equipment immediately

## Slide 11: Your Role in Fall Prevention
Stay alert and aware of surroundings
Follow procedures and use equipment properly
Speak up about unsafe conditions
Participate in training and refreshers
Protect yourself — and your coworkers

## Slide 12: Closing Message
Falls are preventable.
With the right equipment, training, and mindset, we can eliminate fall hazards and protect every worker — every shift.
Stay safe. Stay alert. Stay protected.